Synergetic Daily Aerosol Optical Depth and Type

HDF file explanation

General

Name convention: synaer_env_<ORBIT>.hdf

Format: HDF4

1 Dataset: AEROCLOUD

Product level: 2 (geophysical parameters in orbit projection)

Lines: subsequent pixel numbers along orbit

Column entries

Latitude			for pixel center

Longitude			for pixel center

Latitude/longitude		for 4 pixel corners

Pixel number			along orbit ordering after SCIAMACHY acquisition

Pixel type			indicates availability of EURAD vertical profile correction

(0: no file, 2: file, but outside region, 1: correction was used)

Acquisition date		YYYYMMDD

Acquisition time		HHMMSS.SSS

Solar zenith angle

observer zenith angle

relative azimuth angle

category			result of ambiguity test relevant for aerosol type (see below)

AOD (=AOT)			aerosol optical depth (=thickness) at 550 nm

Aerosol type			number of most plausible aerosol type according to table 1

Cloud fraction			percentage cloud cover in the SCIAMACHY pixel

AOD550 error			absolute standard deviation due to non-unique aerosol type

PM10, PM2.5, PM0.5		particulate mass concentrations near the surface

derived from SYNAER AOD and type

using vertical correction from EURAD over Europe (pixtype=1)

or assuming a 2km homogeneous boundary layer (pixtype=0, 2)

land surface albedo 670	retrieved land surface albedo at 670 nm in SCIAMACHY pixel

water surface albedo 670	retrieved water surface albedo at 670 nm in SCIAMACHY pixel

surface type			surface type number (see below) associated due to 3-λ albedo

fit error			least square fit error in retrieval

category explanation

0				unique aerosol type retrieved

1, 2				few similar aerosol types retrieved:

less than 10% difference per component

and/or different relative humidity

3, 4				several related aerosol types retrieved

less than 20% difference per component

and/or different relative humidity

5, 6				no significant aerosol type retrieval was achieved

surface type explanation

SAVA		savannah					Kriebel

MOOR	bog						Kriebel

WIES		pasture						Kriebel

WALD 	pine forest					Kriebel

LAMA 	LaMancha (mixed)				Kriebel

ACKE 	plowed field					Köpke/Kriebel

HIBE		agriculture (Hildesheimer Börde)		Kriebel

SAND 	sand						Guzzi

SNOW 	fresh snow					Guzzi

SOIL 		bare soil					Guzzi

VEGE 		vegetation					Guzzi

WATE		open water					Guzzi